## Slide 1
Quantum-Safe MACsec on Junos EVO with embedded PhioTX
Docker KME inside each router • ETSI GS QKD 014 • fully orchestrated from one Linux host
Linux server 10.38.98.181 — orchestrator + external CA | hybrid: qkd_net (ipvlan 10.38.96.0/19)
KME phiotx01
10.38.112.21:8443
PostgreSQL
10.38.112.20
KME phiotx02
10.38.112.22:8443
EVO1 10.38.97.218 (Junos EVO)
Docker phiotx01 (PhioTX 4.6.3)
OOB 10.38.112.10 • internal 9.1.1.10
SAE1 sae-001 — on-box runtime (ETSI client)
ETSI 014 mTLS :443
keychain QKD_CA_EVO1_EVO2 • et-0/0/1
EVO2 10.38.97.228 (Junos EVO)
Docker phiotx02 (PhioTX 4.6.3)
OOB 10.38.112.11 • internal 9.1.1.11
SAE2 sae-002 — on-box runtime (ETSI client)
ETSI 014 mTLS :443
keychain QKD_CA_EVO1_EVO2 • et-0/0/1
Hive :9002 • ML-KEM-1024 protected
MACsec (same CAK, MKA Secured)
hybrid only: key-fetch over ETSI 014 + mTLS (hierarchical_ca)
• SAE1 enc_keys → key + key_ID ▸ SAE2 dec_keys(key_ID) → same key ▸ both routers install it as CAK; rolling 4-slot keyring, SSH identity rotation
• One orchestrator (qkd_docker_orchestrator.py): create • bootstrap • phiotx-up • deploy • clean — licences = fleet limit, external CA PKI, idempotent re-runs

## Slide 2
Three application-key modes, one knob: --keygen-mode bulk | pqc | hybrid
Selected at create / bootstrap / phiotx-up / deploy • precedence: CLI > inventory > saved mode > bulk
bulk
bulk
• DRBG (random generator) in phiotx01
• Key copied to phiotx02 over Hive
• No external components
DRBG ──► key K ──► CAK
Validated live: rings, MKA, rotations, 0 errors
PQC-only
pqc(ML-KEM-1024)
• ML-KEM-1024 keypairs + public-key exchange
• KEM shared secret S on both nodes
• SSKDF(S) → key K; no external components
ML-KEM S ──► SSKDF ──► CAK
Validated live: clean + greenfield bootstrap, 0 errors
hybrid
hybrid(ML-KEM-1024)
• PQC secret S + QKD material Q
• Q from 2 ETSI 014 KMEs + 1 PostgreSQL on Linux
• Static IPs .20/.21/.22, hierarchical_ca mTLS
S + Q ──► KDF ──► CAK
Validated live from full clean: hybrid(ML-KEM-1024) + simulated QKD, MKA secured
In every mode the Hive channel between PhioTX containers stays ML-KEM-1024 protected — that is transport protection, not the key-generation mode.
• Hybrid needs no extra PhioTX licences: the KMEs are open ETSI reference simulators (simulated QKD = software random keys, not physical QKD).
• Safety: IP preflight (containers, inventory, ARP), label-scoped clean, qkd_net never created/removed, secrets 0600, no key material printed.
• Next: long-run hybrid soak, failure injection (KME/PostgreSQL outage, Q-pool exhaustion), real QKD KMEs replacing the simulator.